## Slide 1: The Race to Secure Texas Instruments Graphing Calculators
Brandon Wilson

## Slide 2: Who am I?
Calculators got me started in software development / security industry
World’s largest collection

## Slide 3: What is a graphing calculator?
First and foremost – a calculator
Capable of graphing equations
Programmable
  TI-BASIC
  Assembly language (Z80, M68K, ARM, eZ80)
  C
  Python
2.5mm I/O port (sometimes USB)
  Calculator<->calculator communication and sharing of variables
  PC<->calculator communication and sharing of variables, backups, programs, etc.

## Slide 4: The Zilog models
Zilog Z80
6MHz (on some models, up to 15MHz)
8-bit CPU
16-bit addressing (64KB maximum)
8-bit port I/O
  IN/OUT instructions
Anywhere from 32KB RAM all the way up to 128KB
Some have Flash memory, anywhere from 1MB up to 4MB

## Slide 5: The zilog models - ZShell
First model to run assembly programs
  Bets internally at TI on whether we’d figure out a way
OS supports “backups” via TI-Graph Link I/O cable
  Just dumps of system and user RAM
OS also supports “custom” menu entries
  Entries are stored in system RAM as address of OS code handling command
  So…we just change the address to code we place in safe spot of system RAM
    ZShell (program that executes other programs) is started from CUSTOM menu
    Programs as stored as TI-85 “STRING” variables

## Slide 6: The Zilog Models - TI-82
TI-82 also had to be hacked
  No CUSTOM menu
  System RAM has table of handler addresses for system events
    “Context vectors” – handlers for “system contexts” like homescreen, graph screen, etc.
    cxMain vector – keypress handler (if only we could modify it)
  “REAL” variables (numbers) can be copied from one to another (e.g. X->Y, 1->Z)
    REAL variables are 9 bytes
    When storing from one variable to another (X->Y), these 9 bytes are just copied blindly
  PC backups contain system RAM…and user RAM, including pointers to X, Y, etc.
    Modify X’s 9 bytes to contain address of code we want to execute
    Modify Y to point to…cxMain
    X->Y will copy X’s 9 bytes (arbitrary) to cxMain…then press a key, and we have control
  Similar shells exist for TI-82

## Slide 7: The Zilog Models – TI-83/TI-86
TI-83 actually has an assembly program backdoor
  Send( command will send variable to calculator connected to I/O port
    e.g. Send(prgmQUADSOLV
  Send(9 … executes assembly program
    e.g. Send(9prgmSHELL
TI-86 has native assembly program support via Asm( command
  e.g. Asm(prgmGAME
  TI even provided basic documentation for system and user RAM, OS hooks, etc.

## Slide 8: The Zilog Models – Flash Upgradeability
TI-73/Explorer
TI-83 Plus
TI-83 Plus Silver Edition
TI-84 Plus
TI-84 Plus Silver Edition
European-only “improvements”:
  TI-82 Advanced (essentially TI-84 Plus with anti-cheating LED instead of I/O port)
  TI-84 Plus T (essentially TI-84 Plus Silver Edition with anti-cheating LED instead of I/O port)

## Slide 9: The Zilog models – Flash upgradeability
There is no TI-84 (without the “Plus”)
  Until they came out with the “TI-84 Pocket.fr” (which is really a physically-smaller TI-84 Plus)
European duplicates
  TI-82 Stats (really TI-83)
  TI-82 Stats.fr (really TI-83)
  TI-83 Plus.fr (really either TI-83 Plus or TI-84 Plus Silver Edition)
    (yes, they really used the exact same name for two different models)
  TI-82 Plus (really TI-83 Plus)
  TI-82 Advanced (really TI-84 Plus)
  TI-83 Premium CE (essentially TI-84 Plus CE)
  TI-84 Plus T (really TI-84 Plus Silver Edition)

## Slide 10: The Motorola 68k Models
TI-92
TI-92 II
  Also sold expansion modules (TI-92 E, TI-92 II) to convert original TI-92
    Essentially just more RAM and language selections
TI-89 (contains Flash chip and OS/application upgradeability)
TI-92 Plus module (converted TI-92 to TI-92 Plus)
  Added Flash chip, changed it to an entirely different calculator
TI-92 Plus
  TI-92 with Plus module integrated within it)
Voyage 200 (same as TI-92 Plus)
TI-89 Titanium
  Added USB port, minor hardware changes

## Slide 11: The TI-Nspire models (ARM)
TI-Nspire (not NSpire, nSpire, nspire, Inspire, etc.)
  Different swappable keypads (84+, ClickPad, TouchPad)
  TI-84 Plus emulation mode with 84+ keypad
  Both non-CAS and CAS versions
TI-Nspire CX
  Color LCDs
  Both non-CAS and CAS versions
  Chinese variants (slightly less memory)
Completely locked down (no native code)
  Ndless

## Slide 12: The eZ80 Models
TI-84 Plus CE
  eZ80 – 24-bit addressing, Z80 backwards compatibility
    Completely new ASIC (and security design)
  Flat memory model instead of paging/bank switching
  Color LCD
TI-83 Premium CE
  European-only
  Exact math engine
TI-84 Plus CE-T
  European version of TI-84 Plus CE

## Slide 13: Cool things you can do
USB host communication
  Bluetooth adapters
  Serial adapters
  Wi-Fi adapters
  USB flash drives, hard drives, floppy drives, …
  Keyboards and mice
PS3 jailbreak (abuse of USB protocol)
USB device simulation
  Skylanders: Spyro’s Adventure
  Disney Infinity
  Lego Dimensions
  Bootable USB flash drive
  Keyboards and mice

## Slide 14: Why have security in calculators?
Non-free Flash applications
  Games, enhanced math capabilities, other functionality (organizer, periodic table, etc.)
  Creators wouldn’t want these applications copied for free
Anti-cheating functionality
  Disable certain math functions during tests
  Prevent accessing notes/helper programs during tests
Prevent tampering of operating system
  We could make a better OS than TI’s in terms of math, performance, etc.

## Slide 15: Key Players in Security Race
Texas Instruments
  Pressure from educational institutions/teachers
  Prevent cheating during tests, games during class
  TestGuard
  Press-to-Test
The user community
  Maintain control over hardware we own
  New OSes/math functionality, games, repurposing hardware (USB, Wi-Fi), …
Let’s dig in

## Slide 16: Z80 Model Basics
Flash Chip
ASIC
I/O
CPU
6MHz or 15MHz
RAM
32KB or 48KB or 128KB
1MB
or
2MB
or
4MB

## Slide 17: Z80 Model Basics - CPU
Zilog Z80 8-bit CPU – 6MHZ default, capable of switching to 15MHz
16-bit addressing
  64KB memory map (0x0000 – 0xFFFF)
  Split into 4 16KB “pages”/banks
8-bit I/O addressing
  Ports 0x00 through 0xAF
  ASIC configuration, hardware I/O (LCD, keyboard, USB, etc.), …

## Slide 18: Z80 Model Basics – memory map
0x0000 – 0x3FFF
0x4000 – 0x7FFF
0x8000 – 0xBFFF
0xC000 – 0xFFFF
ROM Page 00
or
ROM Page 7F
Any ROM Page
or
Any RAM Page
Any ROM Page
or
Any RAM Page
Any RAM Page
(Port 0x07)
(Port 0x06)
(Port 0x05)

## Slide 19: Z80 Model Security Basics
Port 0x14 – Flash Protection Control
  Write 0x01 to unlock; 0x00 to (re)lock
  Special sequence must be executed from a “privileged” Flash page:
    nop
    nop
    im 1
    di
    out (14h),a
  Privileged Flash pages: 1C-1F (83+), 3C-3F (84+), 6C-6F and 7C-7F (83+SE/84+SE)
    Boot page(s): 1F (83+), 3F (84+), 6C-6F and 7F (83+SE/84+SE)
    OS pages: 1C-1D (83+), 3C-3D (84+), 7C-7D (83+SE/84+SE)

## Slide 20: Flash Unlocking
OS upgrade loop:
  Receive Flash page:address and OS data
  Boot code unlocks Flash with privileged sequence (and checks for trickery*)
  Writes OS data to Flash page:address
  Boot code relocks Flash with privileged sequence
All Flash-related OS functionality:
  Always unlock Flash, perform simple operation quickly, relock Flash

## Slide 21: Flash Unlocking – Potential trickery
After unlocking Flash, boot code and OS check for:
  SP lies between 0xC000 and 0xFFF8 (meaning last (RAM-only) bank)
  Port 6 (0x4000 – 0x7FFF) contains privileged Flash page (1C/3C/7C – 1F/3F/7F)
  Port 7 (0x8000 – 0xBFFF) contains RAM page 0x01 (what OS considers normal)
  Complements the byte at 0x8000, confirming the bank contains writable RAM page
  Complements the byte at 0xC000, confirming the bank contains writable RAM page

## Slide 22: Flash unlocking – potential trickery
Modifying Flash is complicated
  Requires sequence of memory-mapped commands such (erase, program byte, etc.)
  “xor a \ ld (0000h),a” would NOT work – it is ignored
Example:
  SP = 0x1000 (ROM page 0x00)
  CALL SUBROUTINE
  …
  SUBROUTINE:
    ret
We aren’t returning to after the CALL instruction, we’re returning to 0x8080!

## Slide 23: Flash Protection “quirks”
Privileged sequence needs only to be read, not executed
  This works:
    ld ix,address_of_ED_byte
    ld hl,address_of_F3_byte
    rlc b, (ix+0)
    ld d,(hl)
    out (14h),a
  Bytes fetched from privileged page: DD CB 00 00, ED, 56, F3
    Z80 instruction equivalent: nop (00) \ nop (00) \ im 1 (ED 56) \ di (F3)
  This does not require disabling interrupts or setting IM 1
    We could set an IM 2 interrupt and steal away control…if these bytes were found on a privileged page

## Slide 24: Flash Protection “Quirks”
With release of TI-83 Plus Silver Edition, port 0x05 was added
  Controls last bank of memory map (0xC000 – 0xFFFF)
  …TI did not update the Flash unlock checks to also validate the value of port 0x05
0x0000 – 0x3FFF
ROM Page 00
or
ROM Page 7F
Any ROM Page
or
Any RAM Page
(Port 0x06)
0x4000 – 0x7FFF
0x8000 – 0xBFFF
Any ROM Page
or
Any RAM Page
(Port 0x07)
Any RAM Page
(Port 0x05)
0xC000 – 0xFFFF

## Slide 25: Flash Unlock Exploit
What happens if we swap the same RAM page into the last two banks?
ROM Page 00
ROM Page 7C
(Port 0x06)
RAM Page 01
(Port 0x07)
RAM Page 00
(Port 0x05)

## Slide 26: Flash Unlock Exploit
What happens if we swap the same RAM page into the last two banks?
ROM Page 00
ROM Page 7C
(Port 0x06)
RAM Page 01
(Port 0x07)
RAM Page 01
(Port 0x05)

## Slide 27: Flash Unlock Exploit - Continued
Jump into boot code that unlocks Flash, checks if OS is valid, and relocks Flash
OS valid bit at offset 0x1FE0 in certificate sector – entire byte is 0x00
  This is read into OP1 (0x8478), contained in RAM page 0x01
  0x8478 and 0xC478 (0x8478 + 0x4000) point to the same place now
  Point SP to 0xC478 (last bank) give or take a few words
  When boot code writes to 0x8478, value at 0xC478 (SP – return address) is corrupted
  ex. Return address 0x46E1 becomes 0x00E1
  We can steal control away at 0x00E1 via OS hooks

## Slide 28: “Universal” flash unlock exploit
Port 0x05 trickery only works on 83+SE and up
  83+ has no port 0x05 and is out of luck
Prior exploit requires OS hook to steal control
  Also hard-coding locations in OS (version-specific)
Attack functionality that exists on *all* models
  OS must support receiving of Flash applications from PC
  Flash applications are larger than available RAM, so the OS *must* (in a loop):
    Receive small chunk of Flash application into RAM
    Unlock Flash
    Write the Flash application chunk from RAM to *arbitrary* location in Flash
    Re-lock Flash

## Slide 29: “Universal” Flash unlock Exploit
Z80 IY register is never modified by OS after boot – always 0x89F0 (base of OS bitwise flags)
  Boot code uses IY in _WriteFlash
  Bit 1 of IY+25h determines whether destination (DE) should wrap around to start of 2nd bank (0x4000)

## Slide 30: “Universal” Flash unlock exploit
If flag was set, _WriteFlash would function as _FlashToRam
  Copy chunk of data (such as all 0x80s) over the stack in RAM, and trigger return to 0x8080
But the code itself resets it, so there’s no way to make this happen
  …or is there?
If IY points to Flash, a simple SET/RES Z80 instruction will not have any effect
  Writes to Flash are complex memory-mapped instructions
Point IY to Flash where bit is set, jump into OS app-receiving code, and we’re done!
Fixed easily enough in OS, but there are more where this came from if needed

## Slide 31: RSA PUBLIC key factoring
All 7 Flash-upgradeable models have OS and application 512-bit RSA key
  14 total keys + 1 shared datestamp key
  TI gave us the 83+ application signing (“freeware”) key
RSA’s strength is in inability to factor large (512-bit) number into two prime numbers
One person factored the 83+ OS public key with General Number Field Sieve
  One PC, two months
  TI “silenced” this person (came to house with legal threats)
Community created BOINC (Berkeley Open Infrastructure for Network Computing) distributed computing project
  Factored 13 keys in *one* month without TI knowing

## Slide 32: RSA Public Key factoring - Continued
Wrote signing tools to confirm valid factorings for all models
TI sent DMCA (Digital Millennium Copyright Act) notice
EFF (Electronic Frontier Foundation) stepped in
  TI backed off
TI eventually countered – with secondary 2048-bit RSA key
  Only present in boot code of newly-manufactured calculators (boot code v1.03)
  Because hardware wasn’t designed for this, OS validation (after transfer) now takes SIX MINUTES
    Unacceptable – back to Flash unlock exploits

## Slide 33: Defeating New Signing key
Typical cold boot:
  Boot code initializes hardware
  Checks OS valid marker on sector 0
    If marker is valid (value 0x5A at 0x0056), jump into OS
    If marker is invalid (any other value at 0x0056), wait to receive new, valid OS
Typical OS transfer:
  Invalidate the OS in certificate and erase sector 0 (resets OS valid marker)
  In a loop:
    Receive small chunk of OS into RAM
    Unlock Flash, write small chunk to (bounds-checked) location in Flash, re-lock Flash back
  Validate 512-bit signature (now easily bypassed)
  (this is new) Validate 2048-bit signature
  If all checks passed, mark the OS as valid in sector 0 and certificate

## Slide 34: Defeating New Signing key – validating 2048-bit signature
Unlike the original 512-bit signature, the new one is length-indexed
  e.g. 00 01 <0x100 bytes of signature data>
  If the length is going to be a fixed 0x100 bytes, why length-index it?
  …you guessed it, they don’t check the length
Embed a *really large* signature into OS update
  Boot code will blindly copy signature to 0x8000
  FF FF
  0x8000: <…0x80 bytes of padding…>
  0x8080: <C3 xx xx> (this is a Z80 jump to where payload will be)
  0x8083: <…lots and lots of 0x80s that will totally overwrite RAM and the stack…>
  0xXXXX: <code payload to execute>
Once we get control, do some cleanup (validate the OS ourselves in sector 0 and certificate, jump into newly-written OS)
No custom OS transfer tools required, exploits read-only* boot code

## Slide 35: Boot Code Modification
TI-84 Plus and TI-84 Plus Silver Edition boot sectors are *almost* identical
  In fact, other than the 1MB vs. 2MB Flash chip, they *are* identical…except for one I/O write
  On the 84+, 0x00 is written
  On the 84+SE, 0x01 is written
Both calculators run the same OS
  Bit 0 of I/O port 0x21 is checked all over the place in the OS to determine which model it’s running on

## Slide 36: Boot Code modification - Continued
Flash Pages 0x00 – 0x08
(Lower OS Page Range)
Flash Page 0x3F – 0x40
TI-84 Plus
User Archive (Flash applications, “archived” variables, etc.)
Flash Page 0x3F
(Boot Page)
Privileged
Read-Only
Flash Pages 0x3C – 0x3D
(Upper OS Page Range)
Privileged

## Slide 37: Boot Code modification - Continued
Flash Pages 0x00 – 0x08
(Lower OS Page Range)
Flash Pages 0x7C – 0x7D
(Upper OS Page Range)
Privileged
Flash Page 0x3F – 0x40
TI-84 Plus Silver Edition
User Archive (Flash applications, “archived” variables, etc.)
Flash Page 0x7F
(Boot Page)
Privileged
Read-Only
Flash Page 0x7F – 0x80

## Slide 38: Boot Code modification - Continued
Boot code initially sets this value, but what if we unlock Flash and modify it?
  OS would believe 84+SE is actually 84+ and vice versa
  Fun way to mess with people >:)
Flash Pages 0x00 – 0x08
(Lower OS Page Range)
Flash Pages 0x3C – 0x3F
(Upper OS Page Range and Boot Page)
Flash Page 0x3F – 0x40
TI-84 Plus Silver Edition
User Archive (Flash applications, “archived” variables, etc.)
Flash Pages 0x7C – 0x7D
(Upper OS Page Range)
Privileged
(OS won’t use this anymore)
Flash Page 0x7F
(Boot Page)
Privileged
Read-Only
(OS won’t use this anymore)

## Slide 39: Boot Code modification - Continued
Flash Pages 0x00 – 0x08
(Lower OS Page Range)
Flash Pages 0x3C – 0x3F
(Upper OS Page Range and Boot Page)
Read-Only
Flash Page 0x3F – 0x40
TI-84 Plus Silver Edition
User Archive (Flash applications, “archived” variables, etc.)
Boot code initially sets this value, but what if we unlock Flash and modify it?
  OS would believe 84+SE is actually 84+ and vice versa
  Fun way to mess with people >:)
  Whaaaat?
Flash Page 0x7F
(Boot Page)
Privileged
Writable
Flash Pages 0x7C – 0x7D
(Upper OS Page Range)
Privileged

## Slide 40: Boot Code Modification - Continued
I/O port 0x21 isn’t just a register for holding the hardware model
  …it actually controls the Flash write protection on the “last” sector
We can write to the supposedly-readonly boot sector
To write to 0x7F on an 84+SE:
  Write 0x00 to I/O port 0x21 (effectively making it an 84+ non-SE)
  Perform the Flash sector erase/write
  Restore I/O port 0x21 value back to 0x01 (making it an 84+SE again)
To write to 0x3F on an 84+:
  Write 0x01 to I/O port 0x21 (effectively making it an 84+SE)
  Perform the Flash sector erase/write
  Restore I/O port 0x21 value back to 0x00 (making it an 84+ again)

## Slide 41: TI-84 Plus C Silver Edition
New model with color LCD
Identical to TI-84 Plus/Silver Edition (except for 4MB Flash chip vs. 1/2MB)
  Even uses the same ASIC
4MB Flash chip has different sector layout compared to 1/2MB Flash chip
  Flash pages now range from 0x00 to 0xFF (0x100 * 16KB = 4MB)
  Read-only pages 0x6C-0x6F and 0x7F are now part of the user archive
  So how does TI write to those pages?
    They used our workaround
    Did they get the idea from us?

## Slide 42: TI-84 Plus CE – A new Form of Protection
Uses new eZ80 CPU
  Z80 backwards compatibility*
  16-bit I/O range
  Flat memory model (no more pages to swap into 64KB region)
  0x00XX range is “protected”
    Writes to this range must come from “privileged” region
0x00000 – 0x20000
Boot Region
Read-Only
Privileged
0x20000 – (variable based on OS size)
Operating System
Writable
Privileged
User Archive (Flash applications, “archived” variables, etc.)
(controlled by privileged I/O ports 0x001D – 0x001F)

## Slide 43: TI-84 Plus CE – bypassing protections
With any privileged I/O port write, TI must:
  1. Load a constant value into a register
  2. Write register value to protected I/O port
  3. Immediately verify that register contains the same constant value, or lock up/reset
    Otherwise we could just jump into the boot code at step 2 with our own value
OS size is variable, though; can’t hard-code it
  Set our own register value, jump into boot code at write to I/O port 0x001D
  Then steal away control (interrupts, whatever)

## Slide 44: TI-84 Plus CE – the ultimate fail
eZ80 has backwards compatibility for running code in Z80 mode
  ADL mode has access to 24-bit addressing, etc.
Any individual instruction can run in ADL mode or Z80 mode
In ADL mode, you can call a subroutine that runs in Z80 mode
  When it returns, you’re back in ADL mode
In Z80 mode subroutine, you can have ADL instructions such as OUT/IN
Surely the protection on 0x00XX I/O ports works in both ADL and Z80 mode?

## Slide 45: TI-84 Plus CE – The ultimate Fail
Write FE0000 (really high address) to I/O ports 0x001D-0x001F

## Slide 46: TI-84 Plus CE – The Ultimate fail
…someone should be fired over this
The new models are less secure than the ones from 1997, and they were trying to improve upon it
I/O port protection is likely in ASIC, can’t be fixed through software updates
  After the ASIC re-use with the TI-84 Plus C Silver Edition, there’s evidence to suggest fixing the ASIC is cost-prohibitive – this is likely here to stay
  But if not…there are other ways

## Slide 47: TI-82 Advanced (TI-84 Plus without I/O)
No more assembly program execution
No more Flash applications from PC (only built-in applications)
Resort to the original TI-82 hacks?
  RAM backups?
    Normally only something that happens over 2.5mm I/O port
      TI attached a Press-to-Test LED to this I/O port, so it is no longer useful)
    Unbeknownst to most, RAM backups do work over USB (sort of)
  Custom backup sender from PC
    Backup functionality finally removed with TI-84 Plus T

## Slide 48: Where do we go from here?
Release new exploits
  TI-Nspire – Ndless
  Stay on top of TI-84 Plus CE/TI-83 Premium CE developments
  Method of code execution for TI-82 Advanced and TI-84 Plus T

## Slide 49: In conclusion
Calculators are great educational tools
Do not legal threats intimidate you
The community needs your help
Contact me:
  http://brandonw.net
  brandonlw@gmail.com
  @brandonlwilson
  http://youtube.com/ti83programmer
  http://github.com/brandonlw