## Slide 1: There Goes Your PIN Exploiting Smartphone Sensor Fusion Under Single and Cross User Setting
David Berend, Dr. Shivam Bhasin, Dr. Bernhard Jungk
Temasek Laboratories at Nanyang Technological University
Hardware Assurance Group
28th August, 2018
13th September, 2018

## Slide 2: Background
Smartphones evolved to daily companions

## Slide 3: Background
Equipped with various motion and health sensors

## Slide 4: Background
Sensor data accessible without permission

## Slide 5: Background
Data used to gain insights on private information

## Slide 6: Background
Data used to gain insights on private information

## Slide 7: Scenario
* * 8 7
Install malicous application
Train classification system with sensor data
Measure sensors during password-input
Classify and reconstruct password
Unlock smartphone with classified password

## Slide 8: Implementation
* * 8 7
Save measured sensor data
Preprocess cut data streams
Link sensor data to keys
Train & test classifier

## Slide 9: Our Approach
Four keys combined being classified
Previous work
This work
Keys classified individually
10,000 classes trainable
50 combinations trained
Tested with training data
10 classes trainable
10,000 combinations classifiable
Separate testing with ~500 recordings

## Slide 10: Sensor Success & Algorithmic Performance*
Chart: Success Rate [%]
| Accelerometer | Gyroscope | Magnetometer | Ambient Light | Rotation Vector | Acc/Gyr | All Sensors
Candidate C | 63.2653 | 6.1224 | 20.4082 | 0 | 28.5714 | 74.1497 | 0
Chart: Number of Fitted Sampling Data
| 500 | 1000 | 1500 | 2000 | 2500
Random Forest | 28.7749 | 37.037 | 39.0313 | 39.6011 | 41.8803
Nearest Neighbour | 15.3846 | 19.0883 | 25.0712 | 25.0712 | 30.7692
Gaussian Naive Bayes | 19.6581 | 23.0769 | 23.0769 | 25.641 | 28.2051
MLP Neural Network | 29.9145 | 37.037 | 42.4501 | 45.584 | 46.4387
Random Guessing | 10 | 10 | 10 | 10 | 10
*accumulated success after 20 guesses

## Slide 11: Optimization & Insights*
 | A | B | C | ABC
A | 70.10% |  |  | 79.60%
B |  | 16.70% |  | 30.00%
C |  |  | 17.90% | 20.50%
 | 0 ms | 25 ms | 50 ms
0 ms | 74.10% | 68.70% | 71.40%
25 ms | 78.20% | 70.10% | 72.10%
50 ms | 83.70% | 76.90% | 75.50%
 | AB | BC | CA
A |  | 6.10% | 
B |  |  | 6.70%
C | 5.30% |  | 
Enlarging the data stream of PIN‘s digit
Inclusive and exclusive training
*accumulated success after 20 guesses

## Slide 12: Further Applications
Behavioural Profiling
Tapping
Behaviour
Battery
Leakage
Daily
Cycles

## Slide 13: Implications of AI on Mobile Security
Mobile devices have become powerful enough to run extensive machine learning algorithms themselves
New developed sensors are highly accurate, thus reducing noise and increasing learning potential
Data accessibility is still very high, which causes an open door to private information for the public

## Slide 14: Countermeasures
*accumulated success after 20 guesses
Consumer
OS
Manufacturer
Developer
Randomised keyboard
Disabling sensors during sensitive input
Fast frequency certificate
Disabling background sensor measurement
Raising higher awareness
More permissions to grant
Implementing sensors with less frequency

## Slide 15: Thank You!

## Slide 16: Q&A